## Slide 1: Terrestrial ecotoxicity assessment of metals: a course
Technical University of Denmark
M. Owsianiak, R.K. Rosenbaum, M.Z. Hauschild

## Slide 2
Learning objectives
A participant who has met the objectives of the course will be able to:
Identify processes governing metal fate, accessibility, bioavailability and toxicity in soils
Calculate comparative toxicity potentials of a metal in soil
Utilize this knowledge in regionalized impact assessment

## Slide 3: Course structure
Block 1:
A) Characterization models and modeling metal fate (20 min)
Major fate mechanisms for metals is soil (10 min)
Exercise A: calculate fate factor of Cu in 5 soils using USEtox (10 min)
B) Speciation models and modeling metal exposure (20 min)
Structure of speciation models (10 min)
Exercise B: calculate accessibility and bioavailability factors of Cu in 5 soils using empirical regression models (10 min)

## Slide 4: Course structure
Block 2:
C) Terrestrial ecotoxicity (20 min)
Structure of terrestrial ecotoxicity models (10 min)
Exercise C: calculate effect factor of Cu in 5 soils using terrestrial biotic ligand models (10 min)
D) Calculation of comparative toxicity potentials (20 min)
Introduction to a case study (5 min)
Case study: calculate weighted CTP for Cu emitted from a power plant (15 min)

## Slide 5
Block 1

## Slide 6: Terrestrial ecotoxicity assessment
What is impact on terestrial ecosystem from a metal emitted to air?

## Slide 7: Comparative toxicity potential for organics
  Fate factor (FF)
  how long will a substance stay in soil
  Exposure factor (XF)
  how much of it is available for uptake
  Effect factor (EF)
  how toxic is it to soil organisms

## Slide 8: Comparative toxicity potential for metals (in soil)
  Fate factor (FF)
  how long will a metal stay in soil
  Accessibility factor (ACF)
  how much of it is reactive (in the solid phase)
  Bioavailability factor (BF)
  how much of it is available for uptake (in solution)
  Effect factor (EF)
  how toxic is it to soil organisms

## Slide 9: Characterization models: USEtox
In USEtox, fate is modeled by solving a system of mass balance equations assuming steady state
we will employ USEtox to calculated fate factor of Cu in 5 soils after unit emission to air

## Slide 10: Fate factor
Fate factor (FF) is a residence time (in days) of a metal in top soil (here, first 10 cm) after unit emission to an environmental compartment (here, to air)
deposition
top soil
emission to air
leaching to deep soil and groundwater
runoff to surface water

## Slide 11: Exercise A: Calculate fate factors in USEtox
use soil-specific Kd values because both leaching and runoff depend on Kd (you can look up mass balance equations in the ”Fate” sheet of USEtox)
Emission compartment: continental air; receiving compartment: natural soil
soil | pH | OC (%) | CLAY (%) | Kd (L/kg)
1 | 4 | 8 | 66 | 452
2 | 4 | 0.2 | 11 | 1285
3 | 6.4 | 0.3 | 14 | 2225
4 | 7.5 | 1.03 | 61 | 3463
5 | 5.3 | 9.25 | 11 | 343

## Slide 12: Exercise A: Calculate fate factors in USEtox
Import database for inorganics and change Kd value of Cu
sheet: substance data
Kd values are in column M
Cu
Type in Kd value for your soil

## Slide 13: Exercise A: Calculate fate factors in USEtox
sheet: Run
select Cu
Fate factor:

## Slide 14: Exercise A: Solution
soil | pH | OC (%) | CLAY (%) | Kd (L/kg) | FF (day)
1 | 4 | 8 | 66 | 452 | 20259
2 | 4 | 0.2 | 11 | 1285 | 52880
3 | 6.4 | 0.3 | 14 | 2225 | 83870
4 | 7.5 | 1.03 | 61 | 3463 | 117561
5 | 5.3 | 9.25 | 11 | 343 | 15544

## Slide 15: B) Speciation
Cu can exist in many distinct chemical forms, both in the solid phase and in soil pore water
  toxic
CuSO4·5H2O
CuO·SiO2·2H2O
CuO
Cu0
Cu(NO3)2 (aq)
Cu(OH)2 (aq)
Cu(OH)3-
Cu(OH)4-2
Cu+2
Cu2(OH)2+2
Cu2OH+3
Cu3(OH)4+2
CuCl+
CuCl2 (aq)
CuCl3-
CuCl4-2
CuHSO4+
CuNO3+
CuOH+
CuSO4 (aq)

## Slide 16: B) Speciation models
1. Multisurface models
relatively accurate
data demanding
software needed
2. Empirical regression models
less accurate
require few input data
easy to use
log(Cufree) mol/L
WHAM
log(Cufree) mol/L
EMPIRICAL REGRESSION MODEL

## Slide 17: B) Speciation controls accessibility and bioavailability
Accessibility factor:
Bioavailability factor:

## Slide 18: Exercise B: calculate ACF and BF using empirical regression models
assume that organic matter (OM) contains 50% of organic carbon (OC)
assume Cutotal = 16 mg/kg
Units: [mg/kg] for reactive and total metal; [%] for organic matter (OM); and [%] for CLAY
Units: [mol/L] and [mol/kg] for free ion and reactive metal, respectively; and [%] for organic matter (OM)

## Slide 19: Exercise B: Solution
soil | pH | OC (%) | CLAY (%) | Kd (L/kg) | FF (day) | ACF (kgreactive/kgtotal) | BF (kgfree/ kgreactive)
1 | 4 | 8 | 66 | 452 | 20259 | 0.36 | 2.3E-05
2 | 4 | 0.2 | 11 | 1285 | 52880 | 0.45 | 7.1E-04
3 | 6.4 | 0.3 | 14 | 2225 | 83870 | 0.44 | 1.5E-06
4 | 7.5 | 1.03 | 61 | 3463 | 117561 | 0.35 | 4.6E-08
5 | 5.3 | 9.25 | 11 | 343 | 15544 | 0.49 | 9.3E-07

## Slide 20
Block 2

## Slide 21: C) Terrestrial ecotoxicity modeling
toxic
Cu2+
toxic
Cu2+
H+
non-toxic
1. Free ion activity model (FIAM): toxic response is proportional to free ion activity in soil pore water
2. Biotic ligand model (TBLM): toxic response is proportional to the free ion bound to biotic ligand; H+ and base cations alleviate toxicity by competitive binding
biotic ligand

## Slide 22: C) Effect factor
Effect factor (EF) is the incremental change in the potentially affected fraction (ΔPAF) of biological species in the soil ecosystem due to exposure to the free ion concentration of metal
HC50 (kgfree/m3) is the hazardous free ion concentration affecting 50% of the species, calculated as a geometric mean of free ion EC50 values for individual species.
plants:
invertebrates:
microorganisms:

## Slide 23: Exercise C: calculate EF using terrestrial biotic ligand models
calculate EC50 values from soil properties for 6 species
calculate geometric mean of EC50 values, and thereafter the EF
assume {Mg2+} = 0.0038 mol/l
 |  |  | TBLM parameters, log10(KXBL) (X-cation; BL-biotic ligand) |  |  |  |  |  | 
Metal | Organism | Toxic endpoint | f50 | β | {Me} | {H+} | {Ca2+} | {Mg2+} | { Na+}
Cu | barley (Hordeum vulgare cv. Regina) | BRE: root elongation, 4-d EC50 | 0.05 | 0.96 (0.11) | 7.41 (0.23) | 6.48 (0.26) | - | - | -
Cu | tomato (Lycopersicon esculentum cv. Moneymaker) | TSY: shoot yield, 21-d EC50 | 0.05 | 1.11 (0.16) | 5.65 (0.10) | 4.38 (0.21) | - | - | -
Cu | redworm (Eisenia fetida) | FJP: juvenile production, 4-w EC50 chronic | 0.05 | 0.70 (0.08) | 4.62 (0.12) | 2.97 (0.62) | - | - | -
Cu | springtail (Folsomia candida) | ECP: cocoon production, 4-w EC50 chronic | 0.05 | 1.14 (0.15) | 6.50 (0.25) | 5.9 (0.29) | - | - | -
Cu | soil microbes | GIR: glucose induced respiration, 7-d EC50 | 0.05 | 0.58 (0.07) | 6.69 (0.10) | 7.5 1) | - | - | -
Cu | soil microbes | PNR: potential nitrification rate, 7-d EC50 | 0.05 | 0.78 (0.13) | 4.93 (0.48) | 4.45 (0.58) | - | 1.64 (5.80) | -
Units: [mol/L] for {Mg2+} and {Cu2+}EC50

## Slide 24: Solution:
soil | pH | OC (%) | CLAY (%) | Kd (L/kg) | FF (day) | ACF (kgreactive/kgtotal) | BF (kgfree/ kgreactive) | EF (m3/ kgfree)
1 | 4 | 8 | 66 | 452 | 20259 | 0.36 | 2.3E-05 | 4879
2 | 4 | 0.2 | 11 | 1285 | 52880 | 0.45 | 7.1E-04 | 4894
3 | 6.4 | 0.3 | 14 | 2225 | 83870 | 0.44 | 1.5E-06 | 77079
4 | 7.5 | 1.03 | 61 | 3463 | 117561 | 0.35 | 4.6E-08 | 121942
5 | 5.3 | 9.25 | 11 | 343 | 15544 | 0.49 | 9.3E-07 | 28319

## Slide 25: Comparative toxicity potentials
soil | pH | OC (%) | CLAY (%) | Kd (L/kg) | FF (day) | ACF (kgreactive/kgtotal) | BF (kgfree/ kgreactive) | EF (m3/kgfree) | CTP (m3/kgemitted·day)
1 | 4 | 8 | 66 | 452 | 20259 | 0.36 | 2.3E-05 | 4879 | 817
2 | 4 | 0.2 | 11 | 1285 | 52880 | 0.45 | 7.1E-04 | 4894 | 83736
3 | 6.4 | 0.3 | 14 | 2225 | 83870 | 0.44 | 1.5E-06 | 77079 | 4262
4 | 7.5 | 1.03 | 61 | 3463 | 117561 | 0.35 | 4.6E-08 | 121942 | 231
5 | 5.3 | 9.25 | 11 | 343 | 15544 | 0.49 | 9.3E-07 | 28319 | 201

## Slide 26: D) Case study: calculate weighted CTP for Cu emitted from a power plant
Metal deposition ocurrs mainly within 200 km from the source
Weighting of CTP based on deposition load and relative ocurrence of soils is necessary
soil 1
soil 2
soil 3
soil 4
soil 5
soil | a1 0-1 km | a2 1-100 km | a3 100-200 km
soil 1 | 25 | 58 | 35
Soil 2 | 75 | 37 | 30
Soil 3 | 0 | 0 | 10
Soil 4 | 0 | 0 | 12
Soil 5 | 5 | 5 | 3
% ocurrence of soil i in area a (wsi,ai)

## Slide 27: D) Case study: calculate weighted CTP for Cu emitted from a power plant
assume deposition load as in table below
area | % total mass deposited
0-1 km | 13
1-100 km | 83
100-200 km | 4
% mass deposited in area a (wai)

## Slide 28: Solution
Soil-weighted CTPs in each area:
Area-weighted CTP:
CTP that can be applied in regionalized impact assessment

## Slide 29: Take home messages
Comparative toxicity potentials of metals in soil is controlled by soil properties
Deposition area for airborne metal emissions can be large
Weighting of CTPs should be done based on the relative occurrence of soils